## Slide 1
Crash Course in Mechatronics
Mar. 22, 2014

## Slide 2
Mechatronics
A design process that includes a combination of mechanical engineering, electrical engineering, telecommunications engineering, control engineering and computer engineering

## Slide 3
Why Mechatronics?
To design simpler devices to perform more complex roles and varied functions

## Slide 4
How to Build Using Mechatronics?
Understand Mechanical Aspect
  Actuators
  Power Transmission
Understand Electrical Aspect
  Switches
  Variable Resistors
  Voltage Regulators
  Other sensors
Understanding Digital Logic

## Slide 5
How to Build Using Mechatronics?
Understand Mechanical Aspect
  Actuators
  Power Transmission
Understand Electrical Aspect
  Switches
  Variable Resistors
  Voltage Regulators
  Other sensors
Understanding Digital Logic

## Slide 6
Mechanical Aspect
Actuators

## Slide 7
Actuators
Rotational
  DC Brush Motor
  DC Brushless Motor
  Stepper Motor
  Servo Motor
Linear
  Mechanical
    Lead Screw
    Rack and Pinion
    Cams
  Hydraulic Pistons
  Pneumatic Pistons
  Magnetic

## Slide 8
Actuators
Rotational
  DC Brush Motor
  DC Brushless Motor
  Stepper Motor
  Servo Motor
Linear
  Mechanical
    Lead Screw
    Rack and Pinion
    Cams
  Hydraulic Pistons
  Pneumatic Pistons
  Magnetic

## Slide 9: DC Brush Motor
Pros:
Low initial cost
High reliability
Simple control
Cons:
Life span at high intensity
Maintenance
When to use:
Need simple rotation in either one or two directions
Low to medium intensity applications
Don’t need positional accuracy
Don’t need high efficiency

## Slide 11
Actuators
Rotational
  DC Brush Motor
  DC Brushless Motor
  Stepper Motor
  Servo Motor
Linear
  Mechanical
    Lead Screw
    Rack and Pinion
    Cams
  Hydraulic Pistons
  Pneumatic Pistons
  Magnetic

## Slide 13: DC Brushless Motor
Pros:
Higher torque (vs. brush)
Increased reliability
Longevity
Reduced noise
Efficiency
Cons:
Cost
Need controller or driver
When to use:
Maintenance-free operation
High speeds
High intensity applications
High torque required

## Slide 15
Actuators
Rotational
  DC Brush Motor
  DC Brushless Motor
  Stepper Motor
  Servo Motor
Linear
  Mechanical
    Lead Screw
    Rack and Pinion
    Cams
  Hydraulic Pistons
  Pneumatic Pistons
  Magnetic

## Slide 16: Stepper Motor
Pros:
High positional accuracy
High torque
Cons:
Energy inefficient
Open loop
Need stepper motor driver
When to use:
Positional accuracy required (CNC applications)
Low to medium speeds

## Slide 17
Actuators
Rotational
  DC Brush Motor
  DC Brushless Motor
  Stepper Motor
  Servo Motor
Linear
  Mechanical
    Lead Screw
    Rack and Pinion
    Cams
  Hydraulic Pistons
  Pneumatic Pistons
  Magnetic

## Slide 19: Servo Motor
Pros:
High positional accuracy
Closed loop
High holding torque
Cons:
Limited degree of rotation
Open loop
When to use:
Positional accuracy required
Only need limited degree of motion (latches, shutters, etc.)

## Slide 21: Brushless Servo Motor

## Slide 22
Actuators
Rotational
  DC Brush Motor
  DC Brushless Motor
  Stepper Motor
  Servo Motor
Linear
  Mechanical
    Lead Screw
    Rack and Pinion
    Cams
  Hydraulic Pistons
  Pneumatic Pistons
  Magnetic

## Slide 24
Actuators
Rotational
  DC Brush Motor
  DC Brushless Motor
  Stepper Motor
  Servo Motor
Linear
  Mechanical
    Lead Screw
    Rack and Pinion
    Cams
  Hydraulic Pistons
  Pneumatic Pistons
  Magnetic

## Slide 25: Lead Screw
Pros:
Large load carrying capacity
Simple
Precise
Large mechanical advantage
Cons:
High degree of friction
Inefficient
Backlash
When to use:
Positional accuracy required
Motion is slow to medium
Z-axis motion is common

## Slide 27: Rack and Pinion
Pros:
Less backlash
Cons:
Less efficient mechanical advantage
When to use:
Quick linear action with large displacement

## Slide 29: Cam
Pros:
High positional accuracy
Fast action as long as follower can return to position
Cons:
Limited range of motion
When to use:
Positional accuracy required
Only need limited degree of motion

## Slide 31
Actuators
Rotational
  DC Brush Motor
  DC Brushless Motor
  Stepper Motor
  Servo Motor
Linear
  Mechanical
    Lead Screw
    Rack and Pinion
    Cams
  Hydraulic Pistons
  Pneumatic Pistons
  Magnetic

## Slide 34: Hydraulic Cylinder
Pros:
Heavy duty
Efficient and consistent work
Easy to spot leakage
Works in hot environments
Cons:
Hydraulic fluid is very corrosive
Needs heavy duty structure
Needs pump
When to use:
Extremely high loads are required

## Slide 36
Actuators
Rotational
  DC Brush Motor
  DC Brushless Motor
  Stepper Motor
  Servo Motor
Linear
  Mechanical
    Lead Screw
    Rack and Pinion
    Cams
  Hydraulic Pistons
  Pneumatic Pistons
  Magnetic

## Slide 38: Hydraulic Cylinder
Pros:
Clean
Leakage is not damaging
Cons:
Lower forces
Need compressor
When to use:
Support suspension (gas shocks)
Fast acting linear motion

## Slide 39
Actuators
Rotational
  DC Brush Motor
  DC Brushless Motor
  Stepper Motor
  Servo Motor
Linear
  Mechanical
    Lead Screw
    Rack and Pinion
    Cams
  Hydraulic Pistons
  Pneumatic Pistons
  Magnetic

## Slide 42: Solenoid Actuator
Pros:
Quick
Simple to control
Cons:
Limited range of motion
Binary
When to use:
Binary state (latch on/off)
Fast acting

## Slide 44
Actuators
Rotational
  DC Brush Motor
  DC Brushless Motor
  Stepper Motor
  Servo Motor
Linear
  Mechanical
    Lead Screw
    Rack and Pinion
    Cams
  Hydraulic Pistons
  Pneumatic Pistons
  Magnetic

## Slide 45
How to Build Using Mechatronics?
Understand Mechanical Aspect
  Actuators
  Power Transmission
Understand Electrical Aspect
  Switches
  Variable Resistors
  Voltage Regulators
  Other sensors
Understanding Digital Logic

## Slide 46
How to Build Using Mechatronics?
Understand Mechanical Aspect
  Actuators
  Power Transmission
Understand Electrical Aspect
  Switches
  Variable Resistors
  Voltage Regulators
  Other sensors
Understanding Digital Logic

## Slide 47
Mechanical Aspect
Power Transmission

## Slide 48
Power Transmission
Wheel and Axle
  Gears
  Pulleys
  Belt Drive
  Sprocket and Chain
  Friction Drive
Bearings
  Linear
  Rotational

## Slide 49
Power Transmission
Wheel and Axle
  Gears
  Pulleys
  Belt Drive
  Sprocket and Chain
  Friction Drive
Bearings
  Linear
  Rotational

## Slide 50: Gears
Pros:
Very robust and reliable
Precise
Cons:
Loud
Need to be close to motor
Need to be parallel with motor axle
When to use:
When motion axle is close to motor
Need reliable system

## Slide 51
Power Transmission
Wheel and Axle
  Gears
  Pulleys
  Belt Drive
  Sprocket and Chain
  Friction Drive
Bearings
  Linear
  Rotational

## Slide 52: Pulley System
Pros:
Quiet
Does not need to be parallel with or close to motor axle
Cons:
Slippage
Flexibility
Breakage
When to use:
When rotational accuracy is not required

## Slide 53
Power Transmission
Wheel and Axle
  Gears
  Pulleys
  Belt Drive
  Sprocket and Chain
  Friction Drive
Bearings
  Linear
  Rotational

## Slide 54: Belt Drive
Pros:
Quiet
Does not need to be parallel with or close to motor axle
Precise
Cons:
Breakage
When to use:
When rotational accuracy is required
Long range transmission

## Slide 55
Power Transmission
Wheel and Axle
  Gears
  Pulleys
  Belt Drive
  Sprocket and Chain
  Friction Drive
Bearings
  Linear
  Rotational

## Slide 56: Sprocket and Chain
Pros:
Precise
Does not need to be close to motor axle
Will not slip
Cons:
Need to be greased
Loud
When to use:
When strong power transmission is required
Long range transmission

## Slide 57
Power Transmission
Wheel and Axle
  Gears
  Pulleys
  Belt Drive
  Sprocket and Chain
  Friction Drive
Bearings
  Linear
  Rotational

## Slide 58: Friction Drive
Pros:
Simple
Quiet
Cons:
Need to be parallel and close to motor
Slippage
When to use:
When simple power transmission is required
Motion axle is next to motor axle

## Slide 60
Power Transmission
Wheel and Axle
  Gears
  Pulleys
  Belt Drive
  Sprocket and Chain
  Friction Drive
Bearings
  Linear
  Rotational

## Slide 61
Bearing: constrains relative motion and reduces friction between moving parts to only desired motion

## Slide 62
How to Build Using Mechatronics?
Understand Mechanical Aspect
  Actuators
  Power Transmission
Understand Electrical Aspect
  Switches
  Variable Resistors
  Voltage Regulators
  Other sensors
Understanding Digital Logic

## Slide 63
How to Build Using Mechatronics?
Understand Mechanical Aspect
  Actuators
  Power Transmission
Understand Electrical Aspect
  Switches
  Variable Resistors
  Voltage Regulators
  Other sensors
Understanding Digital Logic

## Slide 64
Electrical Aspect
Switches

## Slide 65
Single Pole Single Throw (SPST)

## Slide 66
SPST
SPDT
DPST
DPDT

## Slide 67
Relays

## Slide 68
Relays
Coil Relay
Pros:
Can handle high currents
Reliable
Cons:
Cannot switch as quickly

## Slide 69
Relays
Magnetic Reed Relay
Pros:
Can switch on/off rapidly
Cons:
Cannot handle too high of currents

## Slide 70
Relays
Solid State Relay
Pros:
Can switch on/off rapidly
Has wide variety of ranges for current ratings

## Slide 71
Transistors

## Slide 72
How to Build Using Mechatronics?
Understand Mechanical Aspect
  Actuators
  Power Transmission
Understand Electrical Aspect
  Switches
  Variable Resistors
  Voltage Regulators
  Other sensors
Understanding Digital Logic

## Slide 73
Electrical Aspect
Variable Resistors

## Slide 74
Potentiometer

## Slide 75
Potentiometer

## Slide 76
How to Build Using Mechatronics?
Understand Mechanical Aspect
  Actuators
  Power Transmission
Understand Electrical Aspect
  Switches
  Variable Resistors
  Voltage Regulators
  Other sensors
Understanding Digital Logic

## Slide 77
Electrical Aspect
Voltage Regulators

## Slide 78
Voltage Regulators
Linear Voltage Regulator
Pros:
Cheap
Easy to use
Cons:
Inefficient (may need heat sinking)

## Slide 79
Voltage Regulators
Switching Voltage Regulator
Pros:
Efficiency
Cons:
Extra cost

## Slide 80
How to Build Using Mechatronics?
Understand Mechanical Aspect
  Actuators
  Power Transmission
Understand Electrical Aspect
  Switches
  Variable Resistors
  Voltage Regulators
  Other sensors
Understanding Digital Logic

## Slide 81
Electrical Aspect
Other sensors

## Slide 82
Photoresistors

## Slide 83
Infrared Proximity Sensor

## Slide 84
Ultrasonic Distance Sensor

## Slide 85
Flex Sensor

## Slide 86
Hall Effect Sensor